## Slide 1: Chapter 4 Protocols and the tcp/ip suite Part_1

## Slide 2: Key Features of a Protocol
Syntax
  Concerns the format of the data blocks, The term syntax refers to the structure or format of the data, meaning the order in which they are presented, for example, some protocol might expect the first 8 bits of data to be the address of the sender, the second 8 bits to be the address of the receiver, and the rest of the stream to be the message itself.
Semantics
  Includes control information for coordination and error handling, The word semantics refers to the meaning of each section of bits. How are a particular pattern to be interpreted, and what action is to be taken based on that interpretation? For example, does an address identify the route to be taken or the final destination of the message?
Timing
  Includes speed matching and sequencing

## Slide 3: Agents Involved in Communication
Applications
  Exchange data between computers (e.g., electronic mail)
Computers
  Connected to networks
Networks
  Transfers data from one computer to another

## Slide 4: 4.1 TCP/IP Concepts

## Slide 5: TCP/IP Layers
Physical layer
Network access layer (data link layer)
Internet layer (network layer)
Host-to-host, or transport layer
Application layer

## Slide 6: 4.2 Protocol Data Units (PDUs) in the TCP/IP Architecture

## Slide 7: TCP/IP Physical Layer
Covers the physical interface between a data transmission device and a transmission medium or network
Physical layer specifies:
  Characteristics of the transmission medium
  The nature of the signals
  The data rate
  Other related matters

## Slide 8: TCP/IP Network Access Layer
Concerned with the exchange of data between an end system and the network to which it's attached
Software used depends on type of network
  Circuit switching
  Packet switching (e.g., X.25)
  LANs (e.g., Ethernet)
  Others

## Slide 9: TCP/IP Internet Layer
Uses internet protocol (IP)
Provides routing functions to allow data to traverse multiple interconnected networks
Implemented in end systems and routers

## Slide 10: TCP/IP Host-to-Host, or Transport Layer
Commonly uses transmission control protocol (tcp)
Provides reliability during data exchange
  Completeness
  Order

## Slide 11: TCP/IP Application Layer
Logic supports user applications
Uses separate modules that are peculiar to each different type of application

## Slide 12: Common TCP/IP Applications
Simple mail transfer protocol (SMTP)
  Provides a basic electronic mail facility
File Transfer Protocol (FTP)
  Allows files to be sent from one system to another
Hypertext Transfer Protocol (HTTP)
  Transfers information for the World Wide Web

## Slide 13: Layers of the OSI Model
Application
Presentation
Session
Transport
Network
Data link
Physical

## Slide 14: 4.3 The OSI Layers

## Slide 15: OSI Application Layer
Provides access to the OSI environment for users
Provides distributed information services

## Slide 16: OSI Presentation Layer
Provides independence to the application processes from differences in data representation (syntax)

## Slide 17: OSI Session Layer
Provides the control structure for communication between applications
Establishes, manages, and terminates connections (sessions) between cooperating applications

## Slide 18: OSI Transport Layer
Provides reliable, transparent transfer of data between end points
Provides end-to-end error recovery and flow control

## Slide 19: OSI Network Layer
Provides upper layers with independence from the data transmission and switching technologies used to connect systems
Responsible for establishing, maintaining, and terminating connections

## Slide 20: OSI Data link Layer
Provides for the reliable transfer of information across the physical link
Sends blocks (frames) with the necessary synchronization, error control, and flow control

## Slide 21: OSI Physical Layer
Concerned with transmission of unstructured bit stream over physical medium
Deals with accessing the physical medium
  Mechanical characteristics
  Electrical characteristics
  Functional characteristics
  Procedural characteristics

## Slide 22: TCP/IP Architecture Dominance
TCP/IP protocols matured quicker than similar OSI protocols
  When the need for interoperability across networks was recognized, only TCP/IP was available and ready to go
OSI model is unnecessarily complex
  Accomplishes in seven layers what TCP/IP does with fewer layers

## Slide 23: 4.4 A Comparison of the OSI and TCP/IP Protocol Architectures

## Slide 24: Elements of Standardization within OSI Framework
Protocol Specification
  Format of protocol data units (PDUs) exchanged
  Semantics of all fields
  Allowable sequence of PDUs
Service Definition
  Functional description that defines what services are provided, but not how the services are to be provided
Addressing
  Entities are referenced by means of a service access point (SAP) like LLC between layers

## Slide 25: Internetworking Terms
Communication network – facility that provides a data transfer service among devices attached to the network
Internet – collection of communication networks, interconnected by bridges/routers
Intranet – internet used by an organization for internal purposes
  Provides key Internet applications
  Can exist as an isolated, self-contained internet

## Slide 26: Internetworking Terms
End System (ES) – device used to support end-user applications or services
Intermediate System (IS) – device used to connect two networks
Bridge – an IS used to connect two LANs that use similar LAN protocols
Router - an IS used to connect two networks that may or may not be similar

## Slide 27: Functions of a Router
Provide a link between networks
Provide for the routing and delivery of data between processes on end systems attached to different networks
Provide these functions in such a way as not to require modifications of the networking architecture of any of the attached subnetworks

## Slide 28: Network Differences Routers Must Accommodate
Addressing schemes
  Different schemes for assigning addresses
Maximum packet sizes
  Different maximum packet sizes requires segmentation
Interfaces
  Differing hardware and software interfaces
Reliability
  Network may provide unreliable service